## Slide 1: Tech Talk Wednesday February 8, 2018
Presented on June 27, 2017 to:

## Slide 2
Risk Management:
Precursor to Effective Management Decision Making

## Slide 3: Risk Assessment Process & Risk Management Elements

## Slide 4: Risk Assessment Process
Risk Identification
Frequency Analysis
Consequence Analysis
Risk Evaluation
Risk Reduction
End
Risk
Acceptable
YES
NO

## Slide 5: Risk Management Elements
Identify | Analysis and Precursor to Decisions | Plan and Manage | Control
Define the risk(s) Organizational Knowledge Group Brainstorming Experience from past Communication with stakeholders, suppliers, related functional areas | Bow Tie Ishikawa Fish Bone diagram Heat Matrix Bayesian Network Modelling | Stakeholder engagement Communication plans Training Resistance management Mitigation measures | Monitor performance metrics Leading and lagging indicators Adjust program as needed

## Slide 6: Bow Tie
* Courtesy Government of Canada

## Slide 7: Bow Tie
* Courtesy Government of Canada
The risk is preceded by a cause, and followed by a consequence.
Risk is the knot of the bow tie and the cause(s) and consequence(s) are the “wings”

## Slide 8: Bow Tie - Adjusting for complexity
* Courtesy Government of Canada
First identify possible scenarios. Consider human, natural, economic and technical causes.
Identify consequences once scenarios are built. Consider property, health, finance, liability, people, environment, stakeholder/customer/public confidence

## Slide 9: Ishikawa Fish Bone Diagram

## Slide 10: Ishikawa Fish Bone Diagram
To break down (in successive layers of detail) root causes that potentially contribute to a particular effect. Suggest using when:
Analyzing and finding the root cause of a complicated problem
When there are many possible causes for a problem
Measurement
Problem

## Slide 11: Ishikawa Fish Bone Diagram
2007 Lexus ES350

## Slide 12: Ishikawa Diagram Example - Toyota Unintended Acceleration Investigation

## Slide 13
Vegetation Management Inadequate
Fault Repaired with Substitute Parts
Substitute Parts not Replaced
Design Specification doesn’t meet duty
Requirement Specification
is Incorrect or Incomplete
Inspection Regime is Inadequate (PE I 1.01)
Bare Overhead Conductors:
Failure due to Conductor Break
- Line to Line
- Line to Ground
- Double/Multiple Line to Ground
Leading Indicators not Effective
Inspection Performed Incorrectly
Associated
Asset
Failure
Pole
Cross Arm
Joints
Insulator
Workmanship Mistakes
Unqualified Operator
Inadequate Training
Security Lapse
& Third Party Damage
Vandalism
Theft
Objects thrown over the conductor wires
Physical Degradation
Procedural
Errors
Mechanical Degradation
Inspection Frequency too Long
Vibration (Wind)
Aeolian Vibration (MD V 1.02)
Abrasion Wear
Fretting
Tensile Break
Service Overloading
Reciprocal Loading
Exceeding Rating
Extended Dormancy
Fatigue
Dampener
Instructions Wrong/Not Followed
Fatigue Break
Annealing (PDA 1.01)
Unassisted Failure
(~360 reported per year)
Assisted Failure
(frequency tbd)
Design
Design Change Management
Vehicle Striking Conductor
Damage from Clashing (MD V 1.03)
Conductor uplift leading to fatigue failure of conductor binding wire (MD V 1.01)
Corrosion Centre Span
Corrosion at Fittings
Installation Damage
Corrosion Throughout
Corrosion
(PD C 1.01)
Laboratory Assessment QA Inadequate (PE I 1.02)
Click and expand images for more detail
Unassisted prioritised causes are identified (AA x.xx) and described further in attached slides
Stay released from ground, not properly installed/compacted
Ocean
Industrial
Crop Dusting
Atmospheric
Galvanic

## Slide 14: Mitigating Risk - Aeolian Vibration Wear
Vibration Recorded on 1272 kcmil
45/7 ACSR Conductor (11 Hertz)
* Courtesy Western Power

## Slide 15: Spiral Vibration Damper
The Spiral Vibration Damper is an “impact” type damper made of a rugged non-metallic material that has a tight helix on one end that grips the conductor or wire. The remaining helixes have an inner diameter that is larger than the conductor or wire, such that they impact during Aeolian vibration activity. The impact pulses from the damper disrupt and negate the motion produced by the wind.

## Slide 16: Heat Maps

## Slide 17: Heat Maps – Dalwallinu Example

## Slide 18
Dalwallinu
Quiz: Where is Dalwallinu?

## Slide 19: Risk Identification
The risk identified is:
• public safety, sections of the power lines have come to the end of their useful life;
• risk of fire resulting from asset failure;
• risk of network outages;
• poor customer service outcomes.

## Slide 20
Risk is
multi-dimensional

## Slide 22: Bayesian Modelling
Not saying this is for everyone.

## Slide 23: Myocardial Infarction and Acute Coronary Bayesian Network
Bayesian Network
Probability Distribution and Interdependent Conditions

## Slide 24: Bayesian Network to Predict Vulnerability to Sea-Level Rise Structure of the Bayesian network used for the study:
* Courtesy U.S. Department of the Interior
U.S. Geological Survey
Climate Change

## Slide 25: Variables Used in the Bayesian network
Bayesian Network to Predict Vulnerability to Sea-Level Rise
* Courtesy U.S. Department of the Interior
U.S. Geological Survey

## Slide 26
* Courtesy U.S. Department of the Interior
U.S. Geological Survey
Variables are Inserted into the Model

## Slide 27: Sample Results
Probability of shoreline change less than -1 m/yr (erosion) calculated using the Bayesian network. The probabilities are color coded and labeled with terms developed by the Intergovernmental Panel on Climate Change.
* Courtesy U.S. Department of the Interior
U.S. Geological Survey
Bayesian Network to Predict Vulnerability to Sea-Level Rise

## Slide 28: Summary
Risk Assessment Process
Risk Management Elements
Bow Tie
Ishikawa Fish Bone Diagram
Heat Matrix
Bayesian Network Modelling

## Slide 29
Thank-You. Questions?